## Slide 1: Physics 120B: Lecture 1
Course Structure
Crash Course for Arduino
Crash Course in C

## Slide 2: Course Structure
MWF Lecture, at least for first 5 weeks
  7% of course grade on participation/attendance
Structured Labs first 4 weeks (building blocks)
  demonstrated performance is 36% of grade
  must adhere to due dates to prevent falling behind
Midterm to demonstrate simple coding, 7% of grade
Creative project second half of quarter (50% of grade)
  final demonstration Friday March 21 (with spectators)
Work in teams of 2 (with few exceptions)
Primary Lab periods: T/W 2−6
  at least 2/3 of “help” will be on hand
  will have access to lab space 24/7
Two TAs: Han Lin, Petia Yanchulova

## Slide 3: Project Rubric
Three principal ingredients
  Measure/Sense/Perceive
    the most physics-related component
  Process/Calculate/Think
    usually via microcontroller
  Act/React/Do
    motors, lights, sound, display
Examples from past (inadequately small sample)
  remote-control type car parallel parks itself
  automatic shifting on bike
  rotating LED sphere changes color/intensity to music
  see http://nnp.ucsd.edu/phy120b/tour_121/ for more

## Slide 4: Why is this a Physics Course?
What about this is physics? Why do we bother?
True that this is not front/center in physics research
BUT…
  learn about sensors
  proficiency with a tool that can help control experiments
  learn some coding in C (well-used language in physics)
  more familiar with practical electronics
  learn team dynamics/communication
  deadlines
  gain confidence in ability to do something unique
Goal is fun enough to motivate real investment
  a necessary ingredient to real learning

## Slide 5: Arduino: This is our Brain in Phys120B
Packaged Microcontroller (ATMega 328)
  lots of varieties; we’ll primarily use Uno and Nano
  USB interface; breakout to pins for easy connections
  Cross-platform, Java-based IDE, C-based language
  Provides higher-level interface to guts of device
Arduino Uno
Arduino Nano

## Slide 6: Arduino Core Capabilities
Arduino makes it easy to:
  have digital input/output (I/O) (14 channels on Uno)
  analog input (6 channels on Uno; 8 on Nano)
  “analog” (PWM) output (6 of the digital channels)
  communicate data via serial (over USB makes easy)
Libraries available for:
  motor control; LCD display; ethernet; SPI; serial; SD cards, and lots more
“Shields” for hardware augmentation
  stepper motor drivers
  LCD display
  GPS receiver
  ethernet, wireless, and lots more

## Slide 7: Why Arduino?
Previous incarnations of this course used the PIC microcontroller from Microchip Technology
Why switch to something new?
Arduino allows Mac/Linux users to have fun
  many students are smart enough to avoid Windows
Arduino is cheap ($25−$35 range is typical)
  so students can afford to play on their own (encouraged!)
Arduino programming usefully transfers to research
  C rather than assembly code
High-level functions mean less time at register/bit level
  more time to learn about sensors, put amazing projects together, rather than dwell on computer engineering
Yet loss of low-level understanding is unfortunate cost

## Slide 8: Mission: Get up to Speed Fast
We’re going to do a crash course this first week to get you going super-fast
Involves some hardware proficiency
  hooking up elements in breadboard, e.g.
But mostly it’s about coding and understanding how to access Arduino functions
Emphasis will be on doing first, understanding later
  not always my natural approach, but four weeks is short
Monday lecture will often focus on upcoming lab
Wed. will elaborate and show in-class examples
Friday may often provide context/background

## Slide 9: Every Arduino “Sketch”
Each “sketch” (code) has these common elements
  // variable declarations, like
  const int LED 13;
  void setup()
  {
  // configuration of pins, etc.
  }
  void loop()
  {
  // what the program does, in a continuous loop
  }
Other subroutines can be added, and the internals can get pretty big/complex

## Slide 10: Rudimentary C Syntax
Things to immediately know
  anything after // on a line is ignored as a comment
  braces { } encapsulate blocks
  semicolons ; must appear after every command
    exceptions are conditionals, loop invocations, subroutine titles, precompiler things like #include, #define, and a few others
  every variable used in the program needs to be declared
    common options are int, float, char, long, unsigned long, void
    conventionally happens at the top of the program, or within subroutine if confined to { } block
  Formatting (spaces, indentation) are irrelevant in C
    but it is to your great benefit to adopt a rigid, readable format
    much easier to read if indentation follows consistent rules

## Slide 11: Example Arduino Code
// blink_LED. . . . . . . slow blink of LED on pin 13
const int LED = 13; // LED connected to pin 13
// const: will not change in prog.
void setup() // obligatory; void->returns nada
{
pinMode(LED, OUTPUT); // pin 13 as output (Arduino cmd)
}
void loop() // obligatory; returns nothing
{
digitalWrite(LED, HIGH); // turn LED ON (Arduino cmd)
delay(1000); // wait 1000 ms (Arduino cmd)
digitalWrite(LED, LOW); // turn LED OFF
delay(1000); // wait another second
}

## Slide 12: Comments on Code
Good practice to start code with descriptive comment
  include name of sketch so easy to relate print-out to source
Most lines commented: also great practice
Only one integer variable used, and does not vary
  so can declare as const
pinMode(), digitalWrite(), and delay() are Arduino commands
OUTPUT, HIGH, LOW are Arduino-defined constants
  just map to integers: 1, 1, 0, respectively
Could have hard-coded digitalWrite(13,1)
  but less human-readable than digitalWrite(LED, HIGH)
  also makes harder to change output pins (have to hunt for each instance of 13 and replace, while maybe not every 13 should be)

## Slide 13: Arduino-Specific Commands
Command reference: http://arduino.cc/en/Reference/HomePage
  Also abbr. version in Appendix C of Getting Started book (2nd ed.)
In first week, we’ll see:
  pinMode(pin, [INPUT | OUTPUT])
  digitalWrite(pin, [LOW | HIGH])
  digitalRead(pin)  int
  analogWrite(pin, [0…255])
  analogRead(pin)  int in range [0..1023]
  delay(integer milliseconds)
  millis()  unsigned long (ms elapsed since reset)

## Slide 14: Arduino Serial Commands
Also we’ll use serial communications in week 1:
  Serial.begin(baud): in setup; 9600 is common choice
  Serial.print(string): string  “example text “
  Serial.print(data): prints data value (default encoding)
  Serial.print(data,encoding)
    encoding is DEC, HEX, OCT, BIN, BYTE for format
  Serial.println(): just like print, but CR & LF (\r\n) appended
  Serial.available()  int (how many bytes waiting)
  Serial.read()  char (one byte of serial buffer)
  Serial.flush(): empty out pending serial buffer

## Slide 15: Types in C
We are likely to deal with the following types
char c; // single byte
int i; // typical integer
unsigned long j; // long positive integer
float x; // floating point (single precision)
double y; // double precision
c = 'A';
i = 356;
j = 230948935;
x = 3.1415927;
y = 3.14159265358979;
Note that the variable c=‘A’ is just an 8-bit value, which happens to be 65 in decimal, 0x41 in hex, 01000001
  could say c = 65; or c = 0x41; with equivalent results
Not much call for double precision in Arduino, but good to know about for other C endeavors

## Slide 16: Changing Types (Casting)
Don’t try to send float values to pins, and watch out when dividing integers for unexpected results
Sometimes, we need to compute something as a floating point, then change it to an integer
  ival = (int) fval;
  ival = int(fval); // works in Arduino, anyhow
Beware of integer math:
  1/4 = 0; 8/9 = 0; 37/19 = 1
  so sometimes want fval = ((float) ival1)/ival2
  or fval = float(ival1)/ival2 //okay in Arduino

## Slide 17: Conditionals
The if statement is a workhorse of coding
  if (i < 2)
  if (i <= 2)
  if (i >= -1)
  if (i == 4) // note difference between == and =
  if (x == 1.0)
  if (fabs(x) < 10.0)
  if (i < 8 && i > -5) // && = and
  if (x > 10.0 || x < -10.0) // || = or
Don’t use assignment (=) in test clauses
  Remember to double up ==, &&, ||
Will execute single following command, or next { } block
  wise to form { } block even if only one line, for readability/expansion
Can combine with else statements for more complex behavior

## Slide 18: If..else construction
Snippet from code to switch LED ON/OFF by listening to a button
BUTTON and LED are simply constant integers defined at the program start
Note the use of braces
  exact placement/arrangement unnec., but be consistent
void loop()
{
val = digitalRead(BUTTON);
if (val == HIGH){
digitalWrite(LED, HIGH);
} else {
digitalWrite(LED, LOW);
}
}

## Slide 19: For loops
Most common form of loop in C
  also while, do..while loops
  associated action encapsulated by braces
k is iterated
  assigned to zero at beginning
  confined to be less than 10
  incremented by one after each loop (could do k += 1)
for(;;) makes infinite loop (no conditions)
x += 1 means x = x + 1; x %= 4 means x = x % 4
  count will go 1, 2, 3, 0, 1, 2, 3, 0, 1, 2 then end loop
int k,count;
count = 0;
for (k=0; k < 10; k++)
{
count += 1;
count %= 4;
}

## Slide 20: #define to ease the coding
#define comes in the “preamble” of the code
  note no semi-colons
  just a text replacement process: any appearance of NPOINTS in the source code is replaced by 10
  Convention to use all CAPs to differentiate from normal variables or commands
  Now to change the number of points processed by that program, only have to modify one line
  Arduino.h defines handy things like HIGH = 0x1, LOW = 0x0, INPUT = 0x0, OUTPUT = 0x1, INPUT_PULLUP = 0x2, PI, HALF_PI, TWO_PI, DEG_TO_RAD, RAD_TO_DEG, etc. to make programming easier to read/code
#define NPOINTS 10
#define HIGHSTATE 1

## Slide 21: Voices from the Past
avoid magnets in projects (2013)
heat sinks are there for a reason (2013)
make circuit diagrams & update changes (2013)
robots are stupid (2013)
use the oscilloscope (2013)
save often, and different drafts (2013)
some lectures are boring, but boring ≠ useless (2013)

## Slide 22: Announcements
Can go to lab right after class to start on kits
  otherwise Tue or Wed at 2PM normal lab start time
Late labs (even by an hour) incur grade-point penalty
  very important (for project) to avoid slippage
  can accelerate by jumping through labs ahead of schedule
Will have midterm to check coding proficiency
Grading scheme:
  50% project (proposal, implementation, success, report)
  36% weekly lab (4 installments: success/demo, write-up)
  7% midterm (coding example)
  7% participation/attendance of lecture

## Slide 23: Course Website
Visit http://www.physics.ucsd.edu/~tmurphy/phys120b/
  Assignments
  Lab Exercises
  Useful Links
  Contact Info & Logistics