## Slide 1: Physics 120B: Lecture 10
Under the Arduino Hood

## Slide 2: Arduino Makes it Look Easy
High-level functions remove user/programmer from processor details
  on the plus side, this means you can actually get things done without a steep learning curve
  on the down side, you don’t understand fundamentally what your actions are doing…
  …or how to take advantage of processor capabilities that are not wrapped into high-level functions
So today, we’ll look a bit into what Arduino is actually doing—to a limited extent!

## Slide 3: Where Do the Monsters Lurk?
What I will call the root directory is at:
  On a Mac:
    /Applications/Arduino.app/Contents/Resources/Java/hardware/arduino/
  On Windows:
    Arduino-Install-Directory/Hardware/Arduino/
  On Linux:
    (likely) /usr/share/arduino/
    also may check /usr/local/
I’ll describe contents as found on the Mac
  it’s what I have
  hopefully is reasonably universal

## Slide 4: Contents of root directory
On my Mac, the aforementioned directory has:
  boards.txt has specific info for the various Arduino boards
cores/ has only a directory called arduino/, which we will investigate later
bootloaders/ has
variants/ has
  each of which contains a single file: pins_arduino.h
  maps pinouts of specific devices
boards.txt cores/ programmers.txt
bootloaders/ firmwares/ variants/
atmega/ atmega8/ bt/ caterina/ lilypad/ optiboot/ stk500v2/
eightanaloginputs/ leonardo/ mega/ standard/

## Slide 5: File Types in “Standard” C Programming
Source Code
  the stuff you type in: has .c extension, or .cpp for C++
Compiled “Executable”
  the ready-to-run product: usually no extension in Unix/Mac, .exe in DOS
Header Files
  contain definitions of useful functions, constants: .h extension
Object Files
  a pre-linked compiled tidbit: .o in Unix, .obj in DOS
  only if you’re building in pieces and linking later

## Slide 6: In root/cores/arduino/
Here’s what I show, broken out by extension
  I have 36 files total in this directory, all .c, .cpp, or .h
First, 6 C files:
  note: numbers apply to vers. 1.0.1: minor changes w/ time
The wc function means word count
  returns number of lines, # of words, # of characters for each file
mojo:arduino$ wc *.c
298 1116 8198 WInterrupts.c
324 1468 9394 wiring.c
282 1133 7374 wiring_analog.c
178 668 4931 wiring_digital.c
69 416 2643 wiring_pulse.c
55 236 1601 wiring_shift.c

## Slide 7: Directory, continued
Now, 12 C++ files:
Note in particular main.cpp: 20 lines of fun
  we’ll look at in a bit
mojo:arduino$ wc *.cpp
233 896 6718 CDC.cpp
519 1677 13772 HID.cpp
428 1442 11400 HardwareSerial.cpp
56 115 1152 IPAddress.cpp
263 798 5216 Print.cpp
270 1137 7277 Stream.cpp
601 1783 14311 Tone.cpp
672 1734 13134 USBCore.cpp
59 265 1649 WMath.cpp
645 1923 14212 WString.cpp
20 22 202 main.cpp
18 41 325 new.cpp

## Slide 8: Header files
Finally, the 18 header files
We’ll look at Arduino.h next
mojo:arduino$ wc *.h
215 677 5690 Arduino.h
26 97 697 Client.h
81 289 2363 HardwareSerial.h
76 419 2978 IPAddress.h
23 42 401 Platform.h
78 328 2462 Print.h
40 207 1332 Printable.h
9 17 111 Server.h
96 584 4005 Stream.h
194 478 5224 USBAPI.h
302 846 7855 USBCore.h
63 236 1872 USBDesc.h
88 691 4180 Udp.h
167 699 4576 WCharacter.h
205 1151 8470 WString.h
515 1535 10379 binary.h
22 62 562 new.h
69 230 1752 wiring_private.h

## Slide 9: Arduino.h
Contains function prototypes, definition of constants, some useful algorithms
Excerpts follow
These are standard C libraries that are being pulled in
  note in particular that the math library is automatically used
#include <stdlib.h>
#include <string.h>
#include <math.h>
#include <avr/pgmspace.h>
#include <avr/io.h>
#include <avr/interrupt.h>
#include "binary.h”

## Slide 10: Arduino.h, continued
Now we have some constants defined
  recall, #define acts as text replacement
  In some cases, to absurd precision!
#define HIGH 0x1
#define LOW 0x0
#define INPUT 0x0
#define OUTPUT 0x1
#define INPUT_PULLUP 0x2
#define true 0x1
#define false 0x0
#define PI 3.1415926535897932384626433832795
#define HALF_PI 1.5707963267948966192313216916398
#define TWO_PI 6.283185307179586476925286766559
#define DEG_TO_RAD 0.017453292519943295769236907684886
#define RAD_TO_DEG 57.295779513082320876798154814105

## Slide 11: Arduino.h, continued
The #define construct can also create useful functions
Some labels shortened to fit on this slide (hi, lo, etc.)
#define min(a,b) ((a)<(b)?(a):(b))
#define max(a,b) ((a)>(b)?(a):(b))
#define abs(x) ((x)>0?(x):-(x))
#define constrain(amt,lo,hi) ((amt)<(lo)?(lo):((amt)>(hi)?(hi):(amt)))
#define round(x) ((x)>=0?(long)((x)+0.5):(long)((x)-0.5))
#define radians(deg) ((deg)*DEG_TO_RAD)
#define degrees(rad) ((rad)*RAD_TO_DEG)
#define sq(x) ((x)*(x))
#define lowByte(w) ((uint8_t) ((w) & 0xff))
#define highByte(w) ((uint8_t) ((w) >> 8))
#define bitRead(value, bit) (((value) >> (bit)) & 0x01)
#define bitSet(value, bit) ((value) |= (1UL << (bit)))
#define bitClear(value, bit) ((value) &= ~(1UL << (bit)))
#define bitWrite(val, bit, bval) (bval ? bitSet(val, bit) : bitClear
(val, bit))

## Slide 12: Arduino.h, continued
Also included are function prototypes
  so that we know what types are expected in function calls
This is just an excerpt, for familiar functions
typedef uint8_t byte; // 8-bit integer, same as char
void pinMode(uint8_t, uint8_t);
void digitalWrite(uint8_t, uint8_t);
int digitalRead(uint8_t);
int analogRead(uint8_t);
void analogReference(uint8_t mode);
void analogWrite(uint8_t, int);
unsigned long millis(void);
unsigned long micros(void);
void delay(unsigned long);
void setup(void);
void loop(void);
long map(long, long, long, long, long);

## Slide 13: root/variants/standard/pins_arduino.h
maps pins to functions—excerpts:
#define NUM_DIGITAL_PINS 20
#define NUM_ANALOG_INPUTS 6
#define analogInputToDigitalPin(p) ((p < 6) ? (p) + 14 : -1)
// ATMEL ATMEGA8 & 168 / ARDUINO
//
// +-\/-+
// PC6 1| |28 PC5 (AI 5)
// (D 0) PD0 2| |27 PC4 (AI 4)
// (D 1) PD1 3| |26 PC3 (AI 3)
// (D 2) PD2 4| |25 PC2 (AI 2)
// PWM+ (D 3) PD3 5| |24 PC1 (AI 1)
// (D 4) PD4 6| |23 PC0 (AI 0)
// VCC 7| |22 GND
// GND 8| |21 AREF
// PB6 9| |20 AVCC
// PB7 10| |19 PB5 (D 13)
// PWM+ (D 5) PD5 11| |18 PB4 (D 12)
// PWM+ (D 6) PD6 12| |17 PB3 (D 11) PWM
// (D 7) PD7 13| |16 PB2 (D 10) PWM
// (D 8) PB0 14| |15 PB1 (D 9) PWM
// +----+

## Slide 14: root/cores/arduino/main.cpp
Simple: initialize, run your setup, start infinite loop and run your loop, keeping a lookout for serial comm
#include <Arduino.h>
int main(void)
{
init();
#if defined(USBCON)
USBDevice.attach();
#endif
setup();
for (;;) {
loop();
if (serialEventRun) serialEventRun();
}
return 0;
}

## Slide 15: Finally, root/boards.txt
Examples for Uno and Nano
Note core, variant
  and CPU speed 16 MHz
uno.name=Arduino Uno
uno.upload.protocol=arduino
uno.upload.maximum_size=32256
uno.upload.speed=115200
uno.bootloader.low_fuses=0xff
uno.bootloader.high_fuses=0xde
uno.bootloader.extended_fuses=0x05
uno.bootloader.path=optiboot
uno.bootloader.file=
optiboot_atmega328.hex
uno.bootloader.unlock_bits=0x3F
uno.bootloader.lock_bits=0x0F
uno.build.mcu=atmega328p
uno.build.f_cpu=16000000L
uno.build.core=arduino
uno.build.variant=standard
nano328.name=Arduino Nano w/ ATmega328
nano328.upload.protocol=arduino
nano328.upload.maximum_size=30720
nano328.upload.speed=57600
nano328.bootloader.low_fuses=0xFF
nano328.bootloader.high_fuses=0xDA
nano328.bootloader.extended_fuses=0x05
nano328.bootloader.path=atmega
nano328.bootloader.file=
ATmegaBOOT_168_atmega328.hex
nano328.bootloader.unlock_bits=0x3F
nano328.bootloader.lock_bits=0x0F
nano328.build.mcu=atmega328p
nano328.build.f_cpu=16000000L
nano328.build.core=arduino
nano328.build.variant=eightanaloginputs

## Slide 16: But the Rabbit Hole Goes Much Farther
Underneath it all is a microprocessor with staggering complexity
  full datasheet (avail via course website) is 567 pages
  summary datasheet (strongly encourage perusal) is 35 pp.
Note in particular in the summary datasheet:
  p. 2 the Uno uses the 28-pin PDIP (upper right)
  read the port descriptions on pp. 3−4, even if foreign
  block diagram p. 5
  register map pp. 7−12
  assembly instruction set pp. 13−15
  can safely ignore pp. 16−35 ;-)

## Slide 18: Assignments/Announcements
Absorb as much as possible from the summary datasheet
Project proposals due end of week (2/7)
  recommend pre-discuss with prof/TA, if haven’t already
Midterm next week (propose Friday, Feb 14)